## Slide 1: Winter Sand Quality Assurance and Storage
Department of Transportation and Infrastructure
Operations Branch
May 2015 – January 2017

## Slide 2: Background
NBDTI plans, designs, operates and maintains an extensive network of 18,785 km of highway
6 Districts with 93 winter depots

## Slide 3: Winter Sand: 301,000 tonnes / year
8.8m (29ft)
11t per DTI truck
27,364 trucks
241km (150mi)
Fredericton to Port Elgin
Montreal to Quebec City
OR
Notes: 10 year average sand usage 301,000 tonnes / year
10 year average salt usage 147,500 tonnes / year

## Slide 4: Problem Statement
Sand was clumping due challenges with storage techniques and quality control.
= Wasted time and fuel
= Wear and tear on equipment
= Risk of increased employee accidents
= Re-sanding roads

## Slide 5: Goal
Develop solution to mitigate sand clumping
Create consistent approach for mixing and application

## Slide 6: Lean Six Sigma Methodology

## Slide 7: True Cost of Sand
 | Cost / t
Average tendered cost of sand (2014/15) | $5
Hauling, equipment rental, manipulating, etc. | $11
Total * | $16
* Does not include additional costs for fuel, maintenance, administration, etc.

## Slide 8: Theories to be tested
Sand covered clumps less
Sand with a moisture content > 6-7% clumps more
Stockpile is the optimal size

## Slide 9: Pilot
4 sites
Screened natural pit & crusher winter sand
Weekly inspection and reporting
VS.
Notes: Selected 4 sites to conduct pilot project (District 3)
Petitcodiac depot – Screened natural pit winter sand
Riverside Albert – Screened crusher winter sand
Indian Mountain depot – Screened crusher winter sand
Parkindale depot – Screened natural pit winter sand

## Slide 10: Sand covered clumps less?
YES
NO
SAMPLE

## Slide 11: Sand with a moisture content > 6-7% clumps more?
YES
NO
SAMPLE

## Slide 12: Optimal Stockpile Size
XX t excess sand = X years worth
YES
NO
MAX
140,000t
excess

## Slide 13: Full Implementation
Covering 33 sites = $31,800
2 Unrolling Devices $3,000 (one-time)
Plastic Covering $4,800 / roll (annually)
Training
Video
Covering
Procedures
Increased
Communication

## Slide 14: 2016/17 Savings
After
Before
-50,000t
$823,033

## Slide 15: Benefits
Appropriately sized inventory
Reduced moisture content
Contributes towards 2019 national target for covering treated abrasives (75% covered)
Notes: Appropriately sized inventory
Reduced moisture content
Performance Indicators and National Targets for the Code of Practice for the Environmental Management of Road Salts in Canada
http://www.ec.gc.ca/lcpe-cepa/default.asp?lang=En&n=8D48A850-1
To ensure that all road organizations in Canada have committed to managing their material storage facilities and to ensure best practices at point sources. Case studies have illustrated an elevation in the quantity of salt leached through uncovered piles of abrasives. 2019 Target = 75%

## Slide 16: Feedback
“Covering our sand was easy … The crew thinks it makes a big difference.” D4 Highway Supervisor
“This will be our 2nd yr covering sand and we won’t be going back to open piles of sand again” D3 Highway Supervisor
“We should have been using this before, what a difference in sand” D3 Division Staff